## Slide 1: TIM-GO Experience in GO Challenge 3
Andy Sun
Iberdrola-Avangrid Professor
Massachusetts Institute of Technology
Notes: Primary goal of short pitch + panel session:
Create excitement around your approach – move towards tech to market (e.g., partnerships)
NOTE:
Each team presentation is 5 minutes. Tight.
This is a fast presentation on who you are, key takeaway points, SOA push, most importantly where you want to go from here – T2M, partnerships, etc.
After the teams’ short pitch, the remaining hour will be for a panel discussion so you will have more time to openly discuss/add to your pitch
And you will also have the poster session

## Slide 2: TIM-GO Team
TIM-GO Team Members
Prof. Andy Sun (PI)
Grid Optimization
Matthew Brun
Thomas Lee
Dirk Lauinger
Real Drivers:
Xin Chen

## Slide 3: Progression of ARPA-E GO Challenges
Disjunctive-SC-ACOPF in Challenge 1
  Single-period AC OPF
  Generator & branch (line & transformer) contingencies
  Preventive & corrective contingency actions
  PV/PQ switching in base & contingency
  Up to 30k bus, 35k brch, 3.5k gen, 22k ctg in 10-45min
SC-UC-ACOPF-LS in Challenge 2
  Flexible load dispatch
  UC decision (1-period both in base-case and ctg)
  Branch switching, shunts switch, tap ratios and angles
  Up to 31.7k bus, 40k brch, 4.6k gen, 3-9k ctg in 5-60min
Notes: Challenge 2 has more discrete decisions, less coupling through continuous variables between two stages

## Slide 4: Progression of ARPA-E GO Challenges
Multiperiod-SC-UC-ACOPF-LS in Challenge 3
  Multi-period UC + AC OPF
  Reserves: real & reactive power, zonal & device
  Line contingency w. DC power flow (a lot of them!)
  “Equal status” of producing and consuming devices
  Branch switching (lines, transformers), tap ratio & angles, switched shunts
  Up to 23k bus, 32k brch, 27k ctg, 48 periods, in 10min, 2hr, 4hr
Notes: Challenge 2 has more discrete decisions, less coupling through continuous variables between two stages

## Slide 5: Key Challenges in GO 3
Large-scale MINLP with
  Spatial coupling: AC power flows, reserves
  Temporal coupling: UC, ramping, max/min energy
  Two-stage coupling: Base case vs contingencies
Stringent timing requirements: 10 min (up to 23k, 12 periods)
Memory constraints: 200GB esp for 23k

## Slide 6: Progression of Our Solution Strategies
Challenge 1:
  Primal solution of ACOPF by a local solver
  Smoothing of PV/PQ switching disjunction
  Contingency selection
  ADMM-based decomposition: base vs contingency
  An ADMM-based Distributed Optimization Method for Solving Security-Constrained AC Optimal Power
  Flow, Gholami, Sun, Zhang, S., Operations Research, 2023

## Slide 7: Progression of Our Solution Strategies
Challenge 2:
  Both base and ctg are MINLP
  UC and LS heuristics to first determine UC & LS solution
    UC Heuristics:
      Heuristic strategy to find a proper level of gen for a given level of load by ranking generators according to average generation; give a marginal cost
      LP-based matching
    Line Switching Heuristics:
      Determine which lines to turn on based on UC heuristics (marginal gen cost)
  Fix UC solution, solve NLP

## Slide 8: Progression of Our Solution Strategies
Challenge 3:
  UC and ACOPF decomposition
    Spatial and temporal decomposition
    Model tightening, acceleration
  Convex relaxations of ACOPF
    Facilitate primal solution
    Get dual bounds for performance gaps
  Contingency cuts
  LS heuristics
    Much faster than solving MISOCP
  Parallel computation and memory management
    Single-node (64-core) multi-threading
    256GB memory, 512GB scratch storage
    Especially useful for 23k

## Slide 9: Test Instances
GO3 has provided many test instances (~600 instances)
Network sizes: 3,14,37,73,600,617,1576,2000,4200,6049,6717,8316,23643
industry cases: 6078
# of time periods:
  8-hr (8 0.25-hr, 8 0.5-hr, 2 1-hr)
  48-hr (48 1-hr)
  7-day (42 4-hr)
Line switching allowed for most cases

## Slide 10: Computational Performance
Our codes’ computational performance statistics:
  Best solution gap: Avg: 103%, Range: [82%, 1195%]
    For 73-bus S4 instances: 15x – 172x better
  Global optimality gap: Avg: 99.4%, Std: 2%
    Extremely close to global optimality for most cases

## Slide 11: Industry Implications
Models and data are realistic:
  Division 1 mimics current ISO/TSO real-time markets with 0.25-hr, 0.5-hr, 2-hr look-ahead: solution time 10 min
  Division 2 mimics day-ahead markets: solution time 2 hr
  Division 3 mimics week-long planning: solution time 4 hr
Current codes capability:
  Robust performance in stringent time limits
  Extremely high quality solutions (98%-99% close to global opt)
  Massive parallelization
Look forward to interacting with industry!

## Slide 12: Future Steps
Some missing features:
  Uncertainty of production and consumption
  Storage dynamics and bidding
  Electricity pricing
  T&D coordination

## Slide 13: Thank You
Dick O’Neill, PNNL team, and all the contributors
All participants to push us and show us what are possible

## Slide 14: Contact Information
Andy Sun
Iberdrola-Avangrid Professor in Electric Power System
Sloan School of Management
Massachusetts Institute of Technology
Email: sunx@mit.edu
Tel: 617-324-7443