## Slide 1
Yong Fu, Ph.D.
Professor
Electrical and Computer Engineering
Mississippi State University
September 07, 2023
DOE ARPA-E Grid Software Annual Meeting
Fast AC Security-Constrained Optimal Power Flow with Unit Commitment on High Performance Computing
YongOptimization Team Members: Dr. Yong Fu, Ms. Yehong Peng, Ms. Fasiha Zainab, Dr. Lin Gong
Preventive Action (GO3 Challenge)
Normal
Contingency
X1 
 X0
 X2
Base
Corrective Action

## Slide 2: GO3 Problems & Challenges
  Market Surplus Objective (for D1, D2, D3)
  Maximize:
  Total Market Surplus = Base Case Market Surplus + Worst Case and Average Case of Post-Contingency Outcomes.
  Constraints
  Bus real and reactive power balance and voltage limits
  Zonal reserve requirements
  Device on-off status and related constraints
  Device real and reactive power flow
  Producing and consuming devices: startup, shutdown, dispatchable power, ramping, reserve, max/min energy over multiple intervals
  Shunt real and reactive power constraints
  AC & DC branch flow limits and penalties
  Post-contingency AC power flow limits and branch overload penalty
  Challenges
  Convergence of nonlinear ACOPF problem
  Speed of large-scale mixed integer UC problem
  Multiple periods study
  Numerous creditable contingencies
  Parallel implementation
  Infeasibility issues (tolerance 1.0e-8!!)
Loads
Generators
SCOPF
& UC
AC Lines
HVDC lines
Phase Shifters
Transformers
Capacitors
Outages
large-scale, mixed-integer, nonlinear, non-convex, and multi-period optimization problem

## Slide 3: Software Tools Used and Developed
  Use OpenMPI 4.1.4 to pass messages among multiple processor cores.
  Use Gurobi (10.0.2) (from Gurobi Optimization) as the MILP solver.
  Use PARDISO (8.0) (from Panua Technologies) as the linear solver.
  Develop Fast Unit Commitment Module
  Develop Multi-period AC Optimal Power Flow Module
  Develop Online Contingency Analysis Module
  Develop Dispatchable Power Flow Module
  Develop codes in C language on Linux (CentOS 7.8.2003)
  Tested the codes on 16 processor cores in a desktop computer with Intel® Core™ i9-12900K processor (3.2 GHz) & 64 processer cores in the PNNL HPC.

## Slide 4: Background - AC-SCOPF with UC Solution
Master Problem
Unit Commitment
Subproblems for Base Case
(Network Security Evaluation)
Subproblems for Contingencies
(Network Security Evaluation)
Schedules
Schedules
Constraints
Constraints
Loop A
Loop B
Unit Commitment: Lagrangian Relaxation based & MIP based
Network Security Evaluation: Linear Sensitivity based & Benders Cut based
* Which one is BEST depends on the system and solution conditions *
LR
MIP
LSF
BD
Y. Fu, Z. Li, and L. Wu, “Modeling and Solution of the Large-Scale Security-Constrained Unit Commitment,” IEEE Transactions on Power Systems, Vol. 28, No. 4, pp. 3524-3533, November 2013

## Slide 5
Comparisons between LR and MIP Methods
Items | Lagrangian Relaxation | Mixed Integer Programming
Modeling Ability | (+) Easily model non-linear cost functions and constraints (+) Good at handling some certain constraints (e.g. minimum ON and OFF time limits for each unit, time-dependent startup costs) (-) Add new Lagrangian multipliers for additional constraints (-) Need a high-level iterative procedure to solve the hydrothermal coordination problem | (-) Approximately linearize non-linear cost functions and constraints (+) Flexibly and accurately model other special constraints (e.g. ramping down and up, maximum number of unit startups) and generating units (e.g. combined cycle units, hydro, energy storages) (+) Adding more constraints into the MIP model does not require extra efforts to the solution algorithm
Feasibility and Optimality | (-) The solution is suboptimal due to the non-convexity of the UC problem (-) Lagrangian multiplier adjustments have to be skillfully managed (-) The inclusion of a large number of multipliers related to more constraints could render the UC optimization more difficult and even impossible to solve as the number of constraints grows (-) Heuristics are generally required to find a feasible solution and tighten the lower bound (-) LR method may result in oscillated solutions in ending iterations. Thus, it is difficult for LR method to improve the suboptimal solution through additional iterations. | (+) The MIP solver could guarantee a solution that is globally optimal or one within a pre-specified optimality gap which represents the absolute relative distance between the best integer solution and the best LP solution (+) No heuristics are involved in the MIP method for finding the feasible solution (+) Given enough calculation time, MIP method can always get a true global optimal solution within a finite number of steps (-) It may take longer by MIP than by LR to find an initial feasible solution

## Slide 6
Comparisons between LR and MIP Methods – Ctd.
Items | Lagrangian Relaxation | Mixed Integer Programming
Solution Stability | (+) Compared to the MIP problem, the LR method has a relatively high stability | (-) There is no way to estimate computing time of the MIP method since many factors (e.g. the problem structure and load level) will impact the speed of finding a solution within a given optimality gap
Computer Resource Consumption | (+) Because the number of state spaces and feasible transitions in dynamic programming for solving single unit commitment is proportional to the number of units and hours, memory demand and CPU time of the LR solution increase almost linearly with the size of UC problem | (-) Memory demand and CPU time of MIP solution are more exponential and case-dependent. Solving MIP problem needs more memory to storage nodes in branch-and-bound tree and more CPU time to do branching and bounding.
Hot Start Capability | (+) It is not necessary to flat-start the Lagrangian iteration process for UC problem since previous values of Lagrangian multipliers can accelerate the convergence of LR solution. | (+) A feasible initial solution can be used to hot-start MIP solver for UC problem. As a result, we may significantly reduce the larger number of branching and save CPU time
Applications | (+) The LR model is a good choice for the reliability analysis due to its fast speed (+) The large-scale problem can be quickly solved by LR | (+) The MIP model can bring more social welfares in electricity markets because of its better solution than that of the LR method (-) The MIP method is not competent to solve the large-scale problem (e.g. long-term studies)

## Slide 7
Comparisons between LSF and BD Methods
Items | Linear Sensitivity Factor | Benders Decomposition
AC Ability | (-) When the problem of power flow failing to converge may occur in the LSF method due to unreasonable generation schedules from the master problem, some heuristics have to be developed to get a feasible power flow solution | (+) Due to slack variables, the Benders cut method can work no matter whether the AC power flow converges.
Violation Constraints | (-) Numerous linear violation constraints for each period per iteration may be generated by the LSF method, which will slow, even worse the next UC solution due to the calculation burden. | (+) The Benders cut method has only one cut (or a predefined limited number in the strong Benders cut method) for each period per iteration - Generally requires more iterations for convergence than the LSF method
Post-Contingency Actions | (-) The conventional power flow based LSF method determines post-contingency actions in the UC problem, which results in more continuous variables in the master problem and more SCUC iterations (-) The OPF based LSF method needs advanced methodology for post-contingency actions and can reduce violations through controls in subproblems | (+) The Benders cut method provides post-contingency actions in hourly transmission network security subproblems
CPU Time | (+) The fast decoupled power flow method or the Newton based OPF can provide a quick solution for the subproblem of the LSF method | (-) The LP-based subproblem of the Benders cut method takes longer CPU time than the subproblem of the LSF method.

## Slide 8: Proposed Fast AC-SCOPF with UC Solution on HPC
Master Problem
Unit Commitment
Multi-Period AC Optimal Power Flow
Online Contingency Analysis
Status
Schedules
Constraints
Master Problem
Unit Commitment
Fast Unit Commitment
Optimizer
Unit Commitment
Optimal Power Flow
Power Flow
Initialization

## Slide 9: Fast Unit Commitment Modeling and Solution
  Challenges
  No historical information, no periodic warm-start point
  Relations between real and reactive power outputs of devices
  Huge amount of binary/continuous variables and constraints
  “Unpredictable” calculation time
  Solutions
  LR-based fast UC and initial study (e.g. base/peak devices, system losses, critical branches) in 100 seconds
  Considering both real power and reactive power constraints for both device- and system- levels
  Including power losses (e.g. 1% - 10% of total loads)
  Remodel MIP-based UC (e.g. 3-binary model to 1-binary model, reduce intermediate variables, combine constraints)
  Lock/Unlock status of devices (e.g. commit devices with high economic & security indices)
  Inactive constraints elimination (e.g. reserve requirements for top peak devices only, branch flow limits for critical branches only)

## Slide 10: Fast Unit Commitment – Examples
Devices | Periods (1-18)
1 2 3 | 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
4 5 6 7 8 | 0 0 0 0 0 0 0 1 1 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 1 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0
9 10 11 | 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1
Ex. 2. Lock/Unlock Device Status
Ex. 1. Fast UC Results
Ex. 4. Without Losses v.s. with losses in the UC model
Ex. 3. Full UC model v.s. Fast UC model
Network | Scenario | Devices | Always ON | Always OFF | Percent
C3E3N00617D1 | 1 | 499 | 486 | 0 | 97.39%
C3E3N01576D1 | 27 | 2066 | 1751 | 315 | 100.00%
C3E3N04224D1 | 131 | 2151 | 1823 | 317 | 99.48%
C3E3N06717D1 | 43 | 5826 | 5405 | 220 | 96.54%
C3S3N08316D1 | 1 | 5583 | 5343 | 215 | 99.55%
C3S3N23643D1 | 3 | 18005 | 13607 | 3934 | 97.42%
C3E3N00617D2 | 1 | 499 | 486 | 0 | 97.39%
C3E3N01576D2 | 36 | 2066 | 1751 | 287 | 98.64%
C3E3N04224D2 | 133 | 2151 | 1806 | 277 | 96.83%
C3E3N06049D2 | 31 | 3774 | 3566 | 163 | 98.80%
C3E2N06717D2 | 21 | 5826 | 5299 | 0 | 90.95%
C3S3N23643D2 | 3 | 18005 | 13531 | 103 | 75.00%
Case | Scenario | Objective | Proposed UC | Improvement
 |  | UC without loss | UC with loss | 
C3E3N01576D2 | 43 | 932,056,193 | 945,714,162 | 1.46%
C3E3N01576D3 | 27 | 1,895,822,714 | 1,910,714,162 | 0.80%
C3E2N02000D1 | 3 | 144,790,849 | 168,059,305 | 16.07%
C3E3N04224D3 | 141 | 1,609,623,469 | 1,615,904,284 | 0.4%
C3E2N06717D1 | 4 | 885,609,928 | 887,013,011 | 0.16%
Case | Scenario | Full UC |  | Fast UC | 
 |  | Objective | Time(s) | Objective | Time(s)
C3E3N00073D2 | 232 | 168,361,64 | 18.6 | 168,366,03 | 3.6
C3E3N00617D2 | 1 | 276,313,50 | 61 | 276,313,50 | 12
C3E3N01576D1 | 27 | 101,598,47 | 12.3 | 101,586,14 | 5
C3E3N04224D2 | 132 | 548,598,93 | 233 | 548,598,55 | 32
C3E3N06049D1 | 31 | 104,509,78 | 51 | 104,509,78 | 8
C3E3N06717D1 | 32 | 155,116,50 | 565 | 155,115,31 | 103
C3E2N06717D3 | 33 | 497,207,532 | 614 | 497,206,457 | 179

## Slide 11: Multi-period ACOPF Modeling and Solution
  Challenges
  Huge amount of continuous variables and nonlinear constraints
  Various requirements on power reserves
  A multiple-period study with coupling constraints between periods
  Reliable and stable nonlinear optimization solver
  Solutions
  Remodel ACOPF (e.g. reduce intermediate variables, combine constraints)
  Eliminate inactive constraints (e.g. Non-critical branch flow limits)
  Add linear sensitivity based branch flow limits for critical contingencies only
  Consider both power generation/consumption and reserve constraints
  Determine power “upper” and “lower” bounds of devices for ramping to decouple multiple-period ACOPF
  Develop a primal-dual interior point method with Pardiso as a linear solver (initial point, sparse matrix techniques, step size updates, scaling, etc.) for single-period ACOPF
  Conduct post-processing modules to improve/verify the results
    Dispatchable power flow (e.g. fast-decoupled, factorization, adjustable power outputs)
    Real Power reserve optimization
    Reactive power reserve optimization

## Slide 12: Multi-Period ACOPF Examples
Chart: Iteration
Ex. 1. ACOPF results without reserves v.s with reserves
Case | Scenario | Without Reserve Constraints ($) | With Reserve Constraints ($) | Improvement
C3E3N00073D2 | 247 | 164,131,075 | 164,140,748 | 0.005%
C3E3N00617D1 | 1 | 45,232,724 | 45,233,847 | 0.002%
C3E3N01576D1 | 27 | 78,319,934 | 91,851,257 | 17.27%
C3E3N04224D1 | 131 | 90,963,158 | 91,404,769 | 0.48%
C3E3N06049D1 | 31 | 93,091,830 | 103,787,071 | 11.48%
Chart: Iteration
Ex. 2. Convergence Performance - C3E3N06717D1 – scenario 43 (bus power mismatch < 1.0e-8, 213 iterations, 124 seconds)

## Slide 13: Online Contingency Analysis
  Challenges
  Many, many creditable contingencies (e.g. 26,870 contingencies for a 23,643-bus network)
  Minimize worst contingency penalty
  A time-consuming task
  Memory issue (e.g. 26,870 contingencies × 48 periods × 33,739 branches)
  Solutions
  Covert nodal power balance based to Shift Factor DC based network model
  Calculate Shift Factor for base network model (SF_base)
  Online update Shift Factor for each contingency (SF_ctgc)
  Model violation constraints for critical branches for critical contingencies
SF for Ctgc
SF for base
Network | Scenario | Contingencies | Speed (Seconds) on 25 cores
C3E3N00617D1 | 1 | 562 | 2
C3E3N01576D1 | 27 | 219 | 2
C3E3N04224D1 | 131 | 2,313 | 18
C3E3N06049D1 | 22 | 3,884 | 11
C3E3N06717D1 | 41 | 2,670 | 13

## Slide 14: Parallel Implementation
  Challenges
  Tradeoff between number of used cores and solution speed
  Communication latency between cores
  Computing load-balancing among cores
  Solutions
  Use 25 cores for D1, D2, and D3
  Provide input data to all cores
  Use a Round-Robin algorithm to allocate tasks
  Conduct dynamic time management
Processor
0
Process Queue:
Mod(PI, P)
=0
Total Processes Queue
P: number of processor
PI: process number index (start from 0)
process
Processor
1
Process Queue:
Mod(PI, P)
=1
Processor
P-1
Process Queue:
Mod(PI, P)
=P-1
Round-Robin algorithm: process choose processor in series and will be back to the first processor if the last processor has been reached.

## Slide 15: Parallel Implementation Tasks
  Multiple Parallel Tasks Implemented on HPC (25 cores)
  Fast unit commitment
  Multi-period AC optimal power flow
  Shift factor calculation (e.g. 33,739 branches × 23,643 buses in 5 sec.)
  Online contingency analysis
  Dispatchable power flow
  Real power reserve optimization
  Reactive power reserve optimization

## Slide 16: Selected Sandbox Testing Results on PNNL HPC
Network Model | Scenario | Obj ($) | Time (sec.) | Buses | Dispatchable Devices | Generators | Shunts | AC Branches | Transformer | Zones | Number of Reactive Power Reserve Zones | Contingencies
 |  |  |  |  | Loads | Generators |  |  |  |  |  | 
 |  |  |  |  | Loads | Generators |  | AC Lines | Transformers | Real Power | Reactive Power | 
617 D1 | 1 | 45,283,755 | 67 | 617 | 405 | 94 | 22 | 723 | 130 | 10 | 10 | 562
1576 D1 | 27 | 101,177,934 | 237 | 1576 | 1451 | 615 | 68 | 2270 | 157 | 2 | 2 | 147
4224 D1 | 146 | 110,229,483 | 198 | 4224 | 1673 | 478 | 436 | 2605 | 225 | 2 | 2 | 2313
6049 D1 | 33 | 153,929,849 | 587 | 6049 | 3368 | 406 | 236 | 4920 | 3086 | 6 | 6 | 3902
6717 D1 | 41 | 138,730,145 | 551 | 6717 | 5095 | 731 | 634 | 7173 | 1967 | 12 | 12 | 2670
8316 D1 | 1 | 1,189,613,087 | 573 | 8316 | 4457 | 1126 | 1179 | 7723 | 4249 | 7 | 7 | 4457
23643 D1 | 3 | 104,073,564 | 550 | 23643 | 11731 | 6274 | 2717 | 23797 | 9942 | 16 | 36 | 26870
73 D2 | 231 | 149,170,894 | 44 | 73 | 51 | 154 | 73 | 105 | 15 | 1 | 1 | 2
617 D2 | 1 | 275,910,712 | 175 | 617 | 405 | 94 | 22 | 723 | 130 | 10 | 10 | 562
1576 D2 | 36 | 649,900,609 | 1174 | 1576 | 1451 | 615 | 68 | 2270 | 157 | 2 | 2 | 147
4224 D2 | 143 | 721,753,756 | 953 | 4224 | 1673 | 478 | 436 | 2605 | 225 | 2 | 2 | 2313
6049 D2 | 32 | 678,057,492 | 2280 | 6049 | 3368 | 406 | 236 | 4920 | 3086 | 6 | 6 | 3902
6717 D2 | 4 | 253,292,298 | 2955 | 6717 | 5095 | 731 | 634 | 7173 | 1967 | 12 | 12 | 2670
8316 D2 | 1 | 7,152,876,939 | 3617 | 8316 | 4457 | 1126 | 1179 | 7723 | 4249 | 7 | 7 | 4457
23643 D2 | 3 | 600,577,211 | 1515 | 23643 | 11731 | 6274 | 2717 | 23797 | 9942 | 16 | 36 | 26870
73 D3 | 237 | 484,916,029 | 19 | 73 | 51 | 154 | 73 | 105 | 15 | 1 | 1 | 2
617 D3 | 1 | 967,805,490 | 180 | 617 | 405 | 94 | 22 | 723 | 130 | 10 | 10 | 562
1576 D3 | 27 | 1,910,332,316 | 842 | 1576 | 1451 | 615 | 68 | 2270 | 157 | 2 | 2 | 147
4224 D3 | 133 | 2,491,802,268 | 814 | 4224 | 1673 | 478 | 436 | 2605 | 225 | 2 | 2 | 2313
6049 D3 | 33 | 2,641,244,724 | 2241 | 6049 | 3368 | 406 | 236 | 4920 | 3086 | 6 | 6 | 3902
6717 D3 | 5 | 898,674,042 | 2275 | 6717 | 5095 | 731 | 634 | 7173 | 1967 | 12 | 12 | 2670
8316 D3 | 1 | 25,010,371,429 | 3110 | 8316 | 4457 | 1126 | 1179 | 7723 | 4249 | 7 | 7 | 4457
23643 D3 | 3 | 2,158,212,495 | 1861 | 23643 | 11731 | 6274 | 2717 | 23797 | 9942 | 16 | 36 | 26870

## Slide 17
Concluding Remarks
  Enjoy DOE APAR-E GO Events
  Thanks GO3 administrative team and software sponsors
  Thanks my team members (Ms. Yehong Peng, Ms. Fasiha Zainab, Dr. Lin Gong)

## Slide 18
fu@ece.msstate.edu
THANK YOU!
ANY QUESTIONS …?
Thank You